## Slide 1: Introduction to TCP/IP
TCP/IP簡介
清華大學電機系 劉靖家
電機系
EE2405 Embedded System Labs

## Slide 2: Internet Protocol Suite
Provide end-to-end data communication specifying how data should be packetized, addressed, transmitted, routed and received.
https://en.wikipedia.org/wiki/Internet_protocol_suite

## Slide 3: TCP/IP Layers
https://technet.microsoft.com/en-us/library/cc958821.aspx

## Slide 4: Network Interface Layer
Responsible for placing TCP/IP packets on the network medium and receiving TCP/IP packets off the network medium.
Can be used to connect differing network types
  LAN: Ethernet and Token Ring
  WAN: X.25 and Frame Relay
Assume unreliable Network Interface

## Slide 5: Internet Layer
Responsible for addressing, packaging, and routing functions.
  The core protocols of the Internet layer are IP, ARP, ICMP, and IGMP.
The Internet Protocol (IP)
  A routable protocol responsible for IP addressing, routing, and the fragmentation and reassembly of packets.
The Address Resolution Protocol (ARP)
  resolution of the Internet layer address to the Network Interface layer address such as a hardware address.
The Internet Control Message Protocol (ICMP)
  providing diagnostic functions and reporting errors due to the unsuccessful delivery of IP packets.
The Internet Group Management Protocol (IGMP)
  management of IP multicast groups.

## Slide 6: Transport Layer
Provide the Application layer with session and datagram communication services.
  The core protocols of the Transport layer are Transmission Control Protocol (TCP) and the User Datagram Protocol (UDP).
TCP
  provides a one-to-one, connection-oriented, reliable communications service. TCP is responsible for the establishment of a TCP connection, the sequencing and acknowledgment of packets sent, and the recovery of packets lost during transmission.
UDP
  provides a one-to-one or one-to-many, connectionless, unreliable communications service. UDP is used when the amount of data to be transferred is small (such as the data that would fit into a single packet), when the overhead of establishing a TCP connection is not desired or when the applications or upper layer protocols provide reliable delivery.

## Slide 7: Application Layer (I)
Widely-known Application layer protocols are those used for the exchange of user information:
  The Hypertext Transfer Protocol (HTTP) is used to transfer files that make up the Web pages of the World Wide Web.
  The File Transfer Protocol (FTP) is used for interactive file transfer.
  The Simple Mail Transfer Protocol (SMTP) is used for the transfer of mail messages and attachments.
  Telnet, a terminal emulation protocol, is used for logging on remotely to network hosts.

## Slide 8: Application Layer (II)
Following Application layer protocols help facilitate the use and management of TCP/IP networks:
  The Domain Name System (DNS) is used to resolve a host name to an IP address.
  The Routing Information Protocol (RIP) is a routing protocol that routers use to exchange routing information on an IP internetwork.
  The Simple Network Management Protocol (SNMP) is used between a network management console and network devices (routers, bridges, intelligent hubs) to collect and exchange network management information.

## Slide 9: Packet Encapsulation
The data is sent down the protocol stack
Each layer adds to the data by prepending headers
22Bytes
20Bytes
20Bytes
4Bytes
64 to 1500 Bytes

## Slide 10: IP
Responsible for end to end transmission
Sends data in individual packets
Maximum size of packet is determined by the networks
  Fragmented if too large
Unreliable
  Packets might be lost, corrupted, duplicated, delivered out of order

## Slide 11: IP addresses
4 bytes
  e.g. 163.1.125.98
  Each device normally gets one (or more)
  In theory there are about 4 billion available
But…

## Slide 12: Routing
How does a device know where to send a packet?
  All devices need to know what IP addresses are on directly attached networks
  If the destination is on a local network, send it directly there

## Slide 13: Routing (cont)
If the destination address isn’t local
  Most non-router devices just send everything to a single local router
  Routers need to know which network corresponds to each possible IP address

## Slide 14: Allocation of addresses
Controlled centrally by ICANN
  Fairly strict rules on further delegation to avoid wastage
    Have to demonstrate actual need for them
Organizations that got in early have bigger allocations than they really need

## Slide 15: IP packets
Source and destination addresses
Protocol number
  1 = ICMP, 6 = TCP, 17 = UDP
Various options
  e.g. to control fragmentation
Time to live (TTL)
  Prevent routing loops

## Slide 16: IP Datagram
Vers
Len
TOS
Total Length
Identification
Flags
Fragment Offset
TTL
Protocol
Header Checksum
Source Internet Address
Destination Internet Address
Options...
Padding
Data...
0
4
8
16
19
24
31
Field Purpose
Vers IP version number
Len Length of IP header (4 octet units)
TOS Type of Service
T. Length Length of entire datagram (octets)
Ident. IP datagram ID (for frag/reassembly)
Flags Don’t/More fragments
Frag Off Fragment Offset
Field Purpose
TTL Time To Live - Max # of hops
Protocol Higher level protocol (1=ICMP,
6=TCP, 17=UDP)
Checksum Checksum for the IP header
Source IA Originator’s Internet Address
Dest. IA Final Destination Internet Address
Options Source route, time stamp, etc.
Data... Higher level protocol data
Notes: 16

## Slide 17: IP Routing
Routing Table
Destination IP address
IP address of a next-hop router
Flags
Network interface specification
Application
Transport
Network
Link
Application
Transport
Network
Link
Network
Link
Source
Destination
Router

## Slide 18: UDP
Thin layer on top of IP
Adds packet length + checksum
  Guard against corrupted packets
Also source and destination ports
  Ports are used to associate a packet with a specific application at each end
Still unreliable:
  Duplication, loss, out-of-orderness possible

## Slide 19: UDP datagram
Destination Port
Source Port
Application data
0
16
31
Checksum
Length
Field Purpose
Source Port 16-bit port number identifying originating application
Destination Port 16-bit port number identifying destination application
Length Length of UDP datagram (UDP header + data)
Checksum Checksum of IP pseudo header, UDP header, and data
Notes: 21

## Slide 20: Typical applications of UDP
  Where packet loss etc is better handled by the application than the network stack
  Where the overhead of setting up a connection isn’t wanted
VOIP
NFS – Network File System
Most games

## Slide 21: TCP
Reliable, full-duplex, connection-oriented, stream delivery
  Interface presented to the application doesn’t require data in individual packets
  Data is guaranteed to arrive, and in the correct order without duplications
    Or the connection will be dropped
  Imposes significant overheads

## Slide 22: Applications of TCP
Most things!
  HTTP, FTP, …
Saves the application a lot of work, so used unless there’s a good reason not to

## Slide 23: TCP implementation
Connections are established using a three-way handshake
Data is divided up into packets by the operating system
Packets are numbered, and received packets are acknowledged
Connections are explicitly closed
  (or may abnormally terminate)

## Slide 24: TCP Packets
Source + destination ports
Sequence number (used to order packets)
Acknowledgement number (used to verify packets are received)

## Slide 25: TCP Segment
Destination Port
Acknowledgment Number
Options...
Padding
Data...
0
4
10
16
19
24
31
Source Port
Window
Len
Sequence Number
Reserved
Flags
Urgent Pointer
Checksum
Field Purpose
Source Port Identifies originating application
Destination Port Identifies destination application
Sequence Number Sequence number of first octet in the segment
Acknowledgment # Sequence number of the next expected octet (if ACK flag set)
Len Length of TCP header in 4 octet units
Flags TCP flags: SYN, FIN, RST, PSH, ACK, URG
Window Number of octets from ACK that sender will accept
Checksum Checksum of IP pseudo-header + TCP header + data
Urgent Pointer Pointer to end of “urgent data”
Options Special TCP options such as MSS and Window Scale
You just need to know port numbers, seq and ack are added
Notes: 27

## Slide 26: TCP : Data transfer
Host
Client
Send Packet 1
Start Timer
Retransmit Packet1
Start Timer
Packet should arrive
ACK should be sent
ACK would normally
Arrive at this time
Receive Packet 1
Send AXK 1
Time Expires
Receive ACK 1
Cancel Timer
Packet Lost
Timer
Timer

## Slide 27: IPv6
128 bit addresses
  Make it feasible to be very wasteful with address allocations
Lots of other new features
  Built-in autoconfiguration, security options, …
Not really in production use yet