## Slide 1: Introduction to Bluetooth
Bluetooth簡介
清華大學電機系 劉靖家
電機系
EE2405 Embedded System Labs

## Slide 2: Introduction
A short range wireless standard for exchange data
Use ISM band from 2.4 to 2.485 GHz
Originally to replace RS-232 (UART).

## Slide 3: Masters, Slaves, and Piconets
Bluetooth networks (piconets)
  Master/slave model
  A master device can be connected to up to 7 different slaves
  Any slave device in the piconet can only be connected to a single master
  The master coordinates communication throughout the piconet
    Only master to slave, no slave to slave

## Slide 5: Bluetooth Addresses and Names
Every Bluetooth device has a unique 48-bit address (BD_ADDR)
  MSB 24 bits are organization unique identifier (OUI)
  LSB 24 bits are unique device ID
Names are identification strings (248 bytes)

## Slide 6: Connection Process
Inquiry
  When initially two Bluetooth devices know absolutely nothing about each other
  One device sends out the inquiry request, and any device listening for such a request will respond with its address, and possibly its name and other information.
Paging (Connecting)
  Paging is the process of forming a connection between two Bluetooth devices using known addresses.
Connection
  After a device has completed the paging process, it enters the connection state.
  While connected, a device can either be actively participating or it can be put into a low power sleep mode.

## Slide 7: Connection Modes
Active Mode – This is the regular connected mode, where the device is actively transmitting or receiving data.
Sniff Mode – This is a power-saving mode, where the device is less active. It’ll sleep and only listen for transmissions at a set interval (e.g. every 100ms).
Hold Mode – Hold mode is a temporary, power-saving mode where a device sleeps for a defined period and then returns back to active mode when that interval has passed. The master can command a slave device to hold.
Park Mode – Park is the deepest of sleep modes. A master can command a slave to “park”, and that slave will become inactive until the master tells it to wake back up.

## Slide 8: Bonding and Pairing
Bonded devices automatically establish a connection whenever they’re close enough.
Bonds are created through one-time a process called pairing.
  Both sides share address, name, profiles and a secret key.
Pairing usually requires an authentication process where a user must validate the connection between devices.
  Eg. 6-digit codes.

## Slide 9: Power Classes
 | Max Output Power | Max Output Power | Max Range
Class 1 | 20 dBm | 100mW | 100m
Class 2 | 4 dBm | 2.5mW | 10m
Class 3 | 0 dBm | 1mW | 1m
Class 4 | -3 dBm | 0.5mW | 50cm

## Slide 10: Bluetooth Profiles
Profiles define what kind of data a Bluetooth module is transmitting
  Serial Port Profile (SPP)
    To replace UART
  Human Interface Device (HID)
    Mice, keyboards, and joysticks
  Headset Profile
  Advanced Audio Distribution Profile (A2DP)
  A/V Remote Control Profile (AVRCP)

## Slide 11: Bluetooth Versions
Bluetooth v1.2
  1.0Mbps (0.7) 10m range
Bluetooth v2.1 + EDR
  3Mbps (2.1)
Bluetooth v3.0 + HS
  Ability to use wifi.
Bluetooth v4.0 and Bluetooth Low Energy
  BLE: 0.27Mbps
Bluetooth v5.0
  BLE: tradeoff speed (up to 2M bps) and range (up to 4X)

## Slide 12: Bluetooth Protocol Stack

## Slide 13: Protocol Stacks
Link Management Protocol (LMP)
  Set up and control of the radio link between two devices
Logical Link Control and Adaptation Protocol (L2CAP)
  Multiplex multiple logical connections between two devices using different higher level protocols.
Service Discovery Protocol (SDP)
  Discover services offered by other devices, and their associated parameters
Radio Frequency Communications (RFCOMM)
  Serial port emulation

## Slide 14: Reference
https://learn.sparkfun.com/tutorials/bluetooth-basics
https://en.wikipedia.org/wiki/Bluetooth
http://www.althos.com/tutorial/Bluetooth-tutorial-title-slide.html