## Slide 1
If you use or reference these slides or the associated textbook, please cite the original authors’ work as follows:
Toulson, R. & Wilmshurst, T. (2016). Fast and Effective Embedded Systems Design - Applying the ARM mbed (2nd edition), Newnes, Oxford, ISBN: 978-0-08-100880-5.
www.embedded-knowhow.co.uk
Chapter 10:
Memory and Data Management

## Slide 2: Memory function types
A microprocessor needs memory for two reasons: to hold its program, and to hold the data that it is working with; we often call these program memory and data memory. To meet these needs there are a number of different semiconductor memory technologies available, which can be embedded on the microcontroller chip.
Memory technology is divided broadly into two types: volatile and non-volatile.
Non-volatile memory retains its data when power is removed, but tends to be more complex to write to in the first place. For historical reasons it is still often called ROM (Read Only Memory). Non-volatile memory is generally required for program memory, so that the program data is there and ready when the processor is powered up.
Volatile memory loses all data when power is removed, but is easy to write to. Volatile memory is traditionally used for data memory; it’s essential to be able to write to memory easily, and there is little expectation for data to be retained when the product is switched off. For historical reasons it is often called RAM (Random Access Memory).

## Slide 3: Essential electronic memory types
In any electronic memory we want to be able to store all the 1s and 0s which make up our data.
A simple one-bit memory is a coin. It is stable in two positions, with either “heads” facing up, or “tails”.
We can try to balance the coin on its edge, but it would pretty soon fall over.
We recognise that the coin is stable in two states, we call this bistable.
It could be said that “heads” represents logic 1, and “tails” logic 0. With 8 coins, an 8-bit number can be represented and stored.
If we had 10 million coins, we could store the data that makes up one photograph of good resolution, but that would take up a lot of space indeed!
There are a number of electronic alternatives to the coin, which take up much less space.
One is to use an electronic bistable (or “flip-flop”) circuit.

## Slide 4: Essential electronic memory types
The two logic circuits shown are stable in only two states, and each can be used to store one bit of data.
VCC

## Slide 5: Essential electronic memory types
There are a number of different types of volatile and non-volatile memory:
RAM SRAM DRAM
Random Access Memory Static RAM
Dynamic RAM
ROM PROM EPROM EEPROM FLASH
Read Only Memory Programmable ROM Electrically Programmable ROM Electrically Erasable PROM
A cheap and rapid form of EEPROM

## Slide 6: Introducing pointers
Before delving into the embedded world of memory and file access, we first need to cover a little C/C++ background on pointers.
Pointers are used to indicate where a particular element or block of data is stored in memory.
When a pointer is defined it can be set to a particular memory address and C/C++ syntax allows us to access the data at that address.
Pointers are required for a number of reasons; one is because the C/C++ standard does not allow arrays of data to be passed to and from functions, so in this case we must use pointers instead.
For example, we may wish to pass an array of 10 data values to a function in order to perform a simple mean average calculation, but in C/C++ this is not possible and causes a syntax error if attempted. Instead, to achieve this, it is necessary to pass a single pointer value as an input argument to the function.
In this instance the pointer essentially describes the memory address of the first element of the data array and is usually accompanied by a single argument that defines the size of the data array in question.

## Slide 7: Defining pointers
Pointers are defined similar to variables but by additionally using the * operator. The following declaration defines a pointer called ptr which points to data of type int:
int *ptr; // define a pointer which points to data of type int
The specific address of a data variable, can also be assigned to a pointer by using the &
operator, for example
7
We can also use the * operator in a program to get the data from a pointer address, for example:
int x = *ptr; // get the contents of location ptr and assign to x
We can also use pointers with arrays, because an array is really just a number of data values stored at consecutive memory locations; for example:
// the first element of the array
int | datavariable=7; // | define | a variable called datavariable with value
int | *ptr; // | define | a pointer which points to data of type int
ptr | = &datavariable;// | assign | the pointer to the address of datavariable
int | array[]={3,4,6,2,8,9,1,4,6}; | // | define | an array of arbitrary values
int | *ptr | // | define | a pointer
ptr | = &array[0]; | // | assign | pointer to the address of

## Slide 8: Using pointers with arrays and functions
/* Program Example 10.5: Pointers example for
an array average function
*/
#include "mbed.h" Serial pc(USBTX, USBRX);
char data[]={5,7,5,8,9,1,7,8,2,5,1,4,6,2,1};
char *dataptr; float average;
float CalculateAverage(char *ptr, char size);
// setup serial comms
// define some input data
//
//
define a floating
pointer for the input data point average variable
// function prototype
int main() { dataptr=&data[0];
average = CalculateAverage(dataptr, pc.printf("\n\rdata = ");
for (char i=0; i<sizeof(data); i++) {
pc.printf("%d ",data[i]);
}
// point to address sizeof(data));
of the first array element
// call function
// loop for each data value
// display all the data values
pc.printf("\n\raverage = %.3f",average);
// display average value
}
// CalculateAverage function definition and
code
float CalculateAverage(char int sum=0;
float mean;
*ptr, char size) {
// variable for calculating the sum of the
// variable for floating point mean value
data
for (char i=0; i<size; i++) { sum=sum + *(ptr+i);
// add all data elements together
}
mean=(float)sum/size;
return mean;
// divide by size and cast to floating point
}

## Slide 9: Useful C/C++ library functions for data control
str stream
An array containing the null-terminated sequence of characters to be written.
Pointer to a FILE object that identifies the stream where the data is to be written (see Section B10 for more information on streams in C/C++.
Indicates that additional formatted arguments may be specified in a list
…
Function | Format | Summary Action
fopen | FILE *fopen(const char *filename, const char *mode); | opens the file of name filename
fclose | int fclose(FILE *stream); | closes a file
fgetc | int fgetc(FILE *stream); | gets a character from a stream
fgets | char *fgets(char *str, int n, FILE *stream); | gets a string of n chars from a stream
fputc | int fputc(int character, FILE *stream); | writes character to a stream
fputs | int fputs(const char *str, FILE *stream); | writes a string to a stream
fprintf | int fprintf(FILE *stream, const char *format, ...); | writes formatted data to a stream
fseek | int fseek(FILE *stream, long int offset, int origin); | moves file pointer to specified location

## Slide 10: Using external memory with the mbed
A flash SD (Secure Digital) card can be used with the mbed via the SPI protocol
Using a micro SD card with a card holder cradle (as shown) it is possible to access the SD card as an external memory
The SD card can be connected to the mbed as shown in the following wiring table:
The following mbed libraries are also required:
SDFileSystem library by Simon Ford. https://developer.mbed.org/users/simon/code/SDFileSystem
FatFileSystem by mbed. https://developer.mbed.org/users/mbed_unsupported/code/FatFileSystem

## Slide 11: Writing data to an SD Card
/* Program Example 10.4: writing data to an SD
card
*/
#include "mbed.h"
#include "SDFileSystem.h"
SDFileSystem sd(PTE3, PTE1, PTE2, PTE4, "sd");
Serial pc(USBTX, USBRX);
// MOSI, MISO, SCLK, CS
int main() {
FILE *File = fopen("/sd/sdfile.txt", if(File == NULL) {
pc.printf("Could not open file for
}
else{
"w");
// open file
// check for file pointer
// error if no pointer
write\n");
pc.printf("SD card file successfully
opened\n"); //
on the SD card");
if pointer ok
}
fprintf(File, "Here's some sample text fclose(File);
// write data
// close file
}

## Slide 12: Chapter quiz questions
What does the term bistable mean?
How many bistables would you expect to find in the mbed’s SRAM?
What are the fundamental differences between SRAM and DRAM type memory?
What are the fundamental differences between EEPROM and Flash type memory?
Describe the purpose of pointers and explain how they used to access the different elements of a data array.
What C/C++ command would open a text file for adding additional text to the end of the current file.
What C/C++ command should be used to open a text file called “data.txt” and read the 12th character.
Give a practical example where data logging is required and explain the practical requirements with regards to timing, memory type and size.
Give one reason why pointers are used for direct manipulation of memory data.
Write the C/C++ code that defines an empty 5 element array called dataarray and a pointer called datapointer which is assigned to the first memory address of the data array.

## Slide 13: Chapter review
Microprocessors use memory for holding the program code (program memory) and the
working data (data memory) in an embedded system.
A coin or a logic flip-flop/bistable can be thought of as a single 1-bit memory device which retains its state until the state is actively changed.
Volatile memory loses its data once power is removed, whereas non-volatile can retain memory with no power. A number of different technologies are used to realise these memory types including SRAM and DRAM (volatile) and EEPROM and Flash (non- volatile).
Pointers point to memory address locations to allow direct access to the data stored at
the pointed location.
Pointers are generally required owing to the fact that C/C++ does not allow arrays of data to be passed into functions
The stdio.h library contains functions that allow us to create, open and close files, as
well as read data from and write data to files.
Files can be created on the mbed for storing and retrieving data
Read further:
Try out the data logging mini-project described in Section 10.7
and formatted text.
An external SD memory card or USB Flash drive can be interfaced with the mbed to allow larger memory.